| Questionnaire Ferjovi custom made cylinder ¦ 1/2 |
| --- |
|  | Date |  |  |  |  |  |
|  | Company name |  |  | Contact person |  |  |
|  | Telephone number |  |  | Fax number |  |  |
|  | Email address |  |  |  |  |  |
|  | Quantities required | 64 pieces |  |  |  |
|  | Required delivery time | Week 48 2014 |  |  |  |
|  | Purpose (mark one or more) |  | Lifting |  |  |  |
|  |  |  | Lowering |  |  |  |
|  |  |  | Horizontal movement |  |  |  |
|  |  |  | Tensioning constructions |  |  |  |
|  |  |  | Load securing (locknut cylinders) |  |  |  |
|  |  |  | Other: ………………………………. |  |  |  |
|  | Specifications / restrictions | Standard Capacity / (existing alternative) |  |
|  |  | Massive cylinders | Hollow cylinders |  |
|  |  |  | 5 |  | 30 |  | 150 |  | 500 |  | 5– |  | 60 |  | (250) |  |
|  |  |  | 10 |  | 50 |  | 200 |  | (600) |  | 17 |  | 100 |  | (300) |  |
|  |  |  | (15) |  | (60) |  | (250) |  | (750) |  | 20 |  | 110 |  |  |  |
|  |  |  | 20 |  | 75 |  | 300 |  |  |  | 45 |  | (150) |  |  |  |
|  |  |  | 25 |  | 100 |  | 400 |  |  |  | (50) |  | (200) |  |  |  |
|  |  | ● | Capacity | 536 | ton (if not in the list) |  |
|  |  | ● | Stroke | 21 | mm |  |
|  | Cylinder + under-pinning aluminium block | ● | Built-in height | 427,50 | mm (if restricted) |  |
|  |  | ● | Outside diameter | 400 | mm (if restricted) |  |
|  |  | ● | Working pressure | .......... | bar (if different from 720 bar) |  |
|  |  | ● | Return | gravity / spring / hydraulic |  |
|  |  | ● | Tilting saddle | yes / no |  |
|  |  | ● | Max weight | .......... | kg (if restricted) |  |
|  |  | ● | Required mounting holes | 4x for assembly under pinning alu block |  |
|  |  | ● | Additional requirements | - Lifting “Rud” eyes - Oil release plug - Stainless steel couplers - Horse shoe shim (34 mm) |  |
|  | Environment |  | Inside |  |  |  |
|  |  |  | Near fresh water |  |  |  |
|  |  |  | Near salt water No |  |  |  |
|  |  |  | Resistant | .......... | (acid) |  |
|  | Type of load |  | 100 % centric |  |  |  |
|  |  |  | Eccentric < 5 % |  |  |  |
|  |  |  | Eccentric 5-10 % |  |  |  |
|  |  |  | Eccentric > 10 % |  |  |  |
| Questionnaire Ferjovi custom made cylinder ¦ 2/2 |
|  | Frequency of use Every 3 month | …… #/hours // …… # hours/day // …… # days/year // …… # year |  |
|  |  | Life expectancy | 20 | years |  |
|  |  | Service interval | 2 | years |  |

Surface treatments:

- Saddle				Nitro carburised treatment

- Stop-ring			Nickel High Phosphorus 40ɥm + Heat treatment,4h on 230°C

- Plunger			Duplex coating (Nickel High Phosphorus 40ɥm + 5ɥm Chrome)

- Cylinder housing		NORSOK system M501

- Aluminium part of the housing	NORSOK system M501

- Colour				RAL2009

# Text boxes

No. 05/01, May 2008

No. 05/01, May 2008